## Slide 1: Energy Estimation Flow
RTL from Chipyard Generator
Golden Gate Compiler
Scan Chain Pass
SRAM Hijack Pass
Other Transforms
HAMMER VLSI Flow (-> syn)
ASAP7 PDK
FPGATop RTL
C++ Headers
Firesim/MIDAS Bridges/Widgets
FPGA Build Flow
F1 Emulation
VCD Dump Files
Voltus GL Energy Estimation
Cycle-by-cycle energy numbers
Mapped Verilog
ASAP7 .lib
.sdf
C++ Driver
RTL Sim (Verilator/VCS)

## Slide 2: Checkpoint 1 (4/10) Goals and Progress
RTL simulation of a simple circuit (Risc/GCD) after default Firesim transformation
  Worked through some build issues, and this seems to work fine. The MIDAS-level RTL simulation works with Verilator for the Risc and GCD midasexamples.
ASAP7 Genus synthesis of the circuit and SRAM macros
  Worked through EE241B Lab 1 which uses HAMMER to synthesize a GCD circuit (w/out SRAMs). Working through Lab 4 which uses HAMMER in the Chipyard environment. Going to add energy estimation support via Voltus via HAMMER for next checkpoint.
Formal mapping of RTL VCD to gate-level VCD
  This doesn’t seem to be necessary as we looked through a Cadence RAK (for Voltus) that can estimate energy for GL netlists with RTL VCDs and automatically map them
Scan-chain stitching and SRAM hijack FIRRTL pass working in RTL simulation
  Still working on understanding the Golden Gate compiler and what each pass does. Recently multiclock support has made the compiler more complex. Probably going to use shadow scan chain technique instead of stitched for less complexity

## Slide 3: Changes to Timeline
Checkpoint 2 (4/24): Sample circuit simulating on F1 FPGA, uArch state dumping, initial energy estimation evaluation
Still need to get the Golden Gate scan chain instrumentation pass working
Not planning to go to FPGA just yet, we’re going to focus on getting VCD dumping working in RTL sim possibly with Rocket before trying the FPGA build flow
We want to run a Rocket MIDAS-level RTL sim with VCD state dumping and state sampling and run the VCD snapshots through Voltus with a synthesized Rocket design
Final Report (5/8): Rocket with Gemmini simulating on F1 FPGA, DRAM interface and Gemmini-specific performance instrumentation, Gemmini energy estimation for pre-written ResNet50 and Mobilenet implementations, DRAMSim2 energy estimation
  Not enough experience to know if all of this is possible. We hope at least to get Rocket with Gemmini in MIDAS-level RTL sim with state dumping and Voltus energy estimation when running a simple matmul ubenchmark and maybe a small DNN